## Slide 1
A Benchmark Comparison of Monocular
Visual-Inertial Odometry Algorithms
for Flying Robots
Jeffrey Delmerico and Davide Scaramuzza
rpg.ifi.uzh.ch
Department of Informatics
Department of Neuroinformatics
Notes: 1

## Slide 2: Monocular visual-inertial odometry (VIO) is popular for state estimation on flying robots.

## Slide 3: But due to power and weight constraints, flying robots must carry single-board computers with limited computational power.
Intel NUC
Odroid XU4
Up Board

## Slide 4: There are many open source or publicly available VIO algorithms
OKVIS
ROVIO
VINS-Mono
but it’s not clear how well these algorithms perform for state estimation with the resource constraints of embedded computers.
SVO+GTSAM
SVO+MSF
MSCKF

## Slide 5
We address the question: Given limited computational resources, what is the best VIO algorithm for flying robot state estimation?
In terms of:
Accuracy
CPU Usage
Memory Utilization
Processing Time

## Slide 6
These algorithms include
loosely-coupled
and tightly-coupled VIO
as well as
filtering-
and optimization-based approaches.
To answer it, we tested all of the publicly available VIO algorithms on the single board computers that are typically found on flying robots.
i7 Laptop (Reference)
Intel NUC
Up Board
Odroid XU4
SVO+MSF
MSCKF
ROVIO
OKVIS
VINS-Mono
SVO+GTSAM
VIO Algorithms
HW Platforms

## Slide 7: We ran each algorithm on the 11 sequences in the EuRoC MAV dataset.

## Slide 8: We evaluated accuracy in pose estimation with two metrics:
Root-Mean-Square Error (RMSE): align full estimated trajectory with ground truth; compute RMSE over all poses.

## Slide 9
Odometric Error: compile error statistics over all sub-trajectories of a given length by aligning the first pose of each one with its corresponding ground truth pose, and measuring the drift at the last pose in the sub-trajectory.

## Slide 10: Odometric error results show the algorithm accuracy and robustness.

## Slide 11: We also measure efficiency in terms of CPU, memory, and processing time.

## Slide 12: RMSE and resource usage give insight into the tradeoffs between accuracy and efficiency.
SVO+MSF: most efficient but least accurate.
OKVIS: consistent performance across all HW platforms, but low update rate on the ODROID.
MSCKF: successful on all sequences, but achieves lower accuracy than more modern algorithms.
ROVIO: tight bound on resource usage, competitive accuracy, but unable to run on Up Board due to its low clock speed.
VINS-Mono: consistently robust and accurate, even more with loop closure enabled, but high resource usage.
SVO+GTSAM: high accuracy and modest resource use, but lack of robustness due to numerical instability in GTSAM optimization.

## Slide 13
rpg.ifi.uzh.ch